QBSOLV(1) User Commands QBSOLV(1)
NAME
qbsolv – minimize the objective function represented by a QUBO
SYNOPSIS
qbsolv -i <input_file.qubo> [-o <output_file> [-w]] [-m] [-T <target_value>] [-t <num_seconds>] [-n <num_repeats>] [-S <subproblem_size>] [-v <verbosity_level>] [-q] [-V] [-h]
DESCRIPTION
qbsolv executes the quadratic unconstrained binary optimization (QUBO) problem in the specified file. It provides bit-vector results that minimize or, optionally, maximize the value of the objective function represented by the QUBO problem. qbsolv typically executes in a hybrid fashion on a classical CPU and a quantum processing unit (QPU).
The problem must be in the QUBO(5) file format and is not limited to the size (number of variables), connectivity pattern, or numerical precision of the D-Wave system on which it will be executed.
OPTIONS
-i <input_file.qubo>
Name of the file (relative or absolute pathname) containing the input QUBO. The “.qubo” extension is by convention.
-o <output_file>
Optional. Name of the file (relative or absolute pathname) to which qbsolv will write results. If no file is specified, results are written to standard output.
-w
Optional, in which case -o must also be specified. Prints the input QUBO matrix and the output result in .csv format to the specified output file.
-m
Optional. Specifies that qbsolv is to return the maximum value of the objective function instead of the minimum (default).
-T <target_value>
Optional. Target value of the objective function, expressed as an integer or floating-point number. When target value is reached, qbsolv stops the optimization process. Usually beneficial to specify only when the optimal value of the objective function has been analytically derived.
-t <num_seconds>
Optional. Number of seconds of elapsed CPU time consumed by the classically executing portion of qbsolv after which it stops the optimization process. The value may be specified as an integer or floating-point value. The elapsed CPU time is only checked after completion of the main loop, so the actual stop time may be more than the value. If options –T or –n are also specified, those limits may (depending on their values) stop qbsolv execution before the timeout is reached. The default value is 2,592,000.0 seconds (30 days).

-n <num_repeats>
Optional. Number of times that qbsolv is to repeat the main loop of the algorithm after a new optimal value is found. This value must be a positive integer. The default value is 40.
-S <subproblem_size>
Optional. Size of the subproblems into which qbsolv is to decompose the QUBO. Use 0 to allow qbsolv to use the most effective size for the target D-Wave system. The default value is 45. Any value greater than zero causes qbsolv to use its internal classical tabu solver instead of the D-Wave system.
-v <verbosity_level>
Optional. Level of verbosity of the output. Values are as follows:
- 0 (default) outputs the number of bits in the solution, the solution itself, and the energy of the solution.
- 1 outputs the same information as above for multiple solutions, if found.
- 2 outputs more detailed information at each step of the algorithm.
-q
Optional. Prints the format of an arbitrary QUBO file and exits without running the program.

-V
Optional. Prints the version number of the qbsolv program and exits without running the program.
-h
Optional. Prints the help message for qbsolv and exits without running the program.
BUGS
Report any bugs to dwsupport@dwavesys.com.
COPYRIGHT
© 2016 D-Wave Systems Inc.
SEE ALSO
qubo(5)